## Slide 1: Ethernet: Switching
Mujahid Tabassum
2024
IPv4 Addressing & Network Layer
By: Mujahid Tabassum - 2025

## Slide 2: Agenda
Network layer
IP Characteristics
IP Addressing
IP Network Mask
Introduction to Routing
  Host Routing
  Router Routing

## Slide 3: Recap: Internet Layer Communication
Internet/Network layer protocols primary function is to move data from one network to another network
Network addresses(IP Addresses) must have a mechanism to locate hosts on different networks
Routers use the network portion of this address to determine which path to use to reach its destination.
Destination IP Address
Source IP Address
Data
Network
Host
Network
Host
IP/Network Packet

## Slide 4: The Network Layer
Provides services to allow end devices to exchange data
IP version 4 (IPv4) and IP version 6 (IPv6) are the principle of network layer communication protocols.
The network layer performs four basic operations:
  Addressing end devices
  Encapsulation
  Routing
  De-encapsulation

## Slide 5: IP Encapsulation
IP encapsulates the transport layer segment.
IP can use either an IPv4 or IPv6 packet and not impact the layer 4 segment.
IP packet will be examined by all layer 3 devices as it traverses the network.
The IP addressing does not change from source to destination.
Note: NAT will change addressing, but will be discussed in a later module.

## Slide 6: Characteristics of IP
IP is meant to have low overhead and may be described as:
  Connectionless
  Best Effort
  Media Independent

## Slide 7: The IP Packet Header
Data
Segment Header
Data
Segment Header
Network Header
Data
Segment Header
Network Header
Frame Header
Frame Trailer
Options(if any)
Notes: The term "hop count" typically refers to the number of network devices (such as routers) an IP packet passes through.
The TTL field in an IPv4 header is a one-byte value, so it can be any number between 0 and 255. The primary purpose of the TTL field is to prevent IP packets from looping indefinitely within a network due to routing loops. Every time an IP packet passes through a router, the TTL value is decremented by one.
Here's a general breakdown of common initial TTL values, depending on the operating system:
Linux/Unix: The default TTL is usually set to 64.
Windows: The default TTL value is typically 128.
Cisco Routers (IOS): The default TTL value when originating an IP packet (e.g., a ping) is 255.

## Slide 8: Aside: IPv4 Limitations
Running out of IPv4 addresses
Because of this, lack of end to end connectivity
  Overcome using private IP addressing and Network Address Translation
NAT is everywhere, but was only intended as a temporary solution
Solution: IPv6
  Increased address space – based on 128 bit address, not 32 bits
  Improved packet handling – simplified header with fewer fields
  Eliminates the need for NAT
IPv4 remains dominant choice for various reasons…
This Photo by UnknownAuthor is licensed under CC BY-SA

## Slide 9: IPv6 Overview
IPv6 was developed by Internet Engineering Task Force (IETF).
IPv6 overcomes the limitations of IPv4.
Improvements that IPv6 provides:
  Increased address space – based on 128-bit address, not 32 bits
  Improved packet handling – simplified header with fewer fields
  Eliminates the need for NAT – since there is a huge amount of addressing, there is no need to use private addressing internally and be mapped to a shared public address

## Slide 10: IPV4 Addressing

## Slide 11: IPv4 Address: Phone number analogy
Phone numbers are like network addresses
051-3025635
Area Code – similar to network portion
Phone number – similar to host portion

## Slide 12: MAC and IP Address
Physical/MAC address
  Flat Addressing Scheme
  "Burned" into Network Interface
  Doesn't change (like a PPS number)
IP Address
  Hierarchical Addressing
  Software defined
  Your devices "mailing" address (ie it usually changes when you move)
You need both...

## Slide 13: MAC is flat addressing
If the Internet was a flat network with only MAC addresses, switches would need to know the billions of MAC addresses or broadcast the frame as an unknown unicast.

## Slide 14: IP is Hierarchical
IP address indicates what network the packet belongs to.
Routers maintain lists of IP network addresses to route the packet to the right network.
SETU

## Slide 15: IPv4 Addressing
Which bits refer to network number???
In the past – Classful IP addressing
  Value of first octet(8 bits) determined the network/host portion
Currently
  Classless IP addressing
  Use a subnet mask to determine network portion of address
Classless IP Addressing is what is used within the Internet and in most internal networks.
IPv4 Address
Network
Host
32 bits

## Slide 16: IPv4 Addressing
IPv4 are 32 bits
Divided into four 8 bit sections (octets)
Typically expressed in Dot Decimal Notation
IPv4 Address
Network
Host
32 bits

## Slide 17: IPv4 Address: Converting from binary to dot decimal notation
128 | 64 | 32 | 16 | 8 | 4 | 2 | 1

## Slide 18: IPv4 Address: Converting from Decimal to Binary
128 | 64 | 32 | 16 | 8 | 4 | 2 | 1

## Slide 19: IPv4 Address: Converting Decimal to Binary
192.168.10.10
192
11000000
168
10101000
10
00001010
10
00001010

## Slide 20: IPv4 Subnet Mask
A subnet mask is a separate 32-bit pattern used to define the network and host portions of an address.
Shows where the network portion is in the IP.
192
11000000
168
10101000
10
00001010
10
00001010
255
11111111
255
11111111
255
11111111
0
00000000
IPv4 address
Subnet Mask
192
11000000
168
10101000
10
00001010
0
00000000
Network address
Subnet mask always has 1s from left to final position of network address. 1s show the location of netawork portion

## Slide 21: IPv4 Address: Subnet Mask – bitwise AND operation
192
11000000
168
10101000
10
00001010
10
00001010
255
11111111
255
11111111
255
11111111
0
00000000
192
11000000
168
10101000
10
00001010
0
00000000
IPv4 address
Subnet Mask
Network address
1 AND 1 = 1
0 AND 1 = 0
0 AND 0 = 0
1 AND 0 = 0

## Slide 22: IP Addressing: Network, Host, Broadcast
Network address (host portion all 0s) – Network
  In opposite example, 192.168.1.0
Broadcast address (host portion all 1s)
  In opposite example, 192.168.1.255
First host address
  192.168.1.1
Last host address
  192.168.1.254

## Slide 23: IP Addressing: Network Address Prefix Length
Alternative way to identify subnet mask.
Known as “slash notation”
Example:
IP Network Address 10.1.0.0/23
Subnet mask is : 255.255.254.0 (11111111.11111111.11111110.00000000)
10.1.0.0 00001010.00000001.00000000.00000000 (network address)
10.1.0.1 00001010.00000001.00000000.00000001 (first host)
10.1.1.254 00001010.00000001.00000001.11111110 (last host)
10.1.1.255 00001010.00000001.00000001.11111111 (broadcast)
Max Number of hosts: 29 –2 = 510 hosts
/23 indicates number of bits "borrowed" for network address
Max number of hosts = 2b-2 where b is the number of bits used for the HOST portion of the IP Address. (take away 2 as you CANNOT use network or broadcast address for hosts.

## Slide 24: First and Last Host Address

## Slide 25: IPv4 Dot Decimal Prefix Notation

## Slide 26: Assigning Static IP to a Host
Windows example

## Slide 27: Assigning Static IP to a Host
Packet Tracer

## Slide 28: Assigning a Dynamic IP address
DHCP - preferred method of “leasing” IPv4 addresses to hosts on large networks, reduces the burden on network support staff and virtually eliminates entry errors

## Slide 29: Routing on a Host
e.g. your computer

## Slide 30: Forwarding: where should it go?
All hosts maintain a Routing Table
The host will send an IP packet to
  Itself – loopback address(127.0.0.1)
  Local Hosts – Same LAN (part of IP) matching network
  Remote Host – On different LAN(different network part of IP)

## Slide 31: Forwarding: where should it go?
The Source device determines whether the destination is local or remote using it’s own IP address and subnet mask and destination IP address
Local destination traffic is sent straight out from interface and is handled by Data-Link/layer 2 devices
Remote traffic is forwarded to Default Gateway
The Defaut Gateway will:
  Have an IP address on LAN
  Accept and route to other networks.
Last Resort Route: if no other route matches
Notes: Source device determines whether the destination is local or remote using it’s own IP address and subnet mask and destination IP address
Local destination traffic is sent straight out from interface and is handled by Data-Link/layer 2 devices
Remote traffic is forwarded to Default Gateway

## Slide 32: Host Routing Table
route print, route or netstat -r will display the host routing table
IP Address: 192.168.10.10
IP Address: 192.168.10.1
Network Address
Default Gateway

## Slide 33: Routers – Packet Forwarding
On receiving frame from host device
  Decapsulates/extracts IP Packet from Ethernet Frame
  Gets IP destination address
  Searches Routing table for best match and finds “next hop”
  Encapsulates IP packet back into Ethernet/Data Link Frame
  Forwards on to next hop device

## Slide 34: IP Routing Table
Routing tables can contain:
  Directly Connected routes: active interfaces automatically added by router
  Remote: Not directly connected but entry made either manually (static route) or Dynamically(routing protocol)
  Default Route: where to send traffic if no other match found.

## Slide 35: Static/Dynamic Routing
Static routes are configured manually
Must be Updated if topology changes
Fine for small, non- redundant networks
Combined with routing protocols for defining default routes.
Dynamic Routing can:
  Discover remote networks
  Exchange routing info with other routers
  Choose the best path to the destination
  Handle topology changes, dropped links.

## Slide 36: IP Addressing: Types

## Slide 37: IP Addressing: Address Types
Public IPv4 addresses are globally routed between internet service provider (ISP) routers.
Private addresses are common blocks of addresses used by most organisations to assign IPv4 addresses to internal hosts.
  Not unique
  Not routed globally
Network | Range (RFC 1918)
10.0.0.0/8 | 10.0.0.0-10.255.255.255
172.2.16.0.0/12 | 172.16.0.0 – 172.31.255.255
192.168.0.0/16 | 192.168.0.0-192.168.255.255

## Slide 38: IP Addressing: NAT
Network Address Translation (NAT) translates private IPv4 addresses to public IPv4 addresses.
NAT usually on router connected to internet(it’s on your home router)
Translates between private and public global IP addresses.

## Slide 39: IP Addressing: History
RFC 790 (1981) allocated IPv4 addresses in classes
  But no medium size networks
Class A/B addresses depleted quickly
Lots of wasted addresses
REPLACED BY CLASSLESS ADDRESSING

## Slide 40: IP Address Assignment
IANA (Internet Assigned Numbers Authority )responsible for global coordination of the Internet Protocol addressing systems. Regional-based and hierarchical...