## Slide 1: Indirect Messaging
Frank Walsh

## Slide 2: Using the “Middleman”
  Communication between processes using an intermediary
    Sender  “The middle-man”  Receiver
    No direct coupling
  Up to now, only considered Direct Coupling
    Introduces a degree of rigidity
  Consider…
    What happens if a device fails during communication in Direct Coupling?
    What if you'd like to add
  Two important properties of intermediary in communication
    Space uncoupling (devices don't need to "know" about each other)
    Time uncoupling (devices don't need to be "available" at the same time)
A
B
A
B
Intermediary
Direct Communication
Indirect Communication

## Slide 3: MQTT
MQ Telemetry Transport (MQTT)
Telemetry
  Remote measurements
Created by IBM
  from message queueing (MQ) architecture used by IBM for service oriented networks.
  Telemetry data goes from devices to a server or broker.
  Uses a publish/subscribe mechanism.
Lightweight both in bandwidth and code footprint

## Slide 4: MQTT – publish subscribe
Topics/Subscriptions: Messages are published to topics.
  Clients can subscribe to a topic or a set of related topics
Publish/Subscribe: Clients can subscribe to topics or publish to topics.

## Slide 5: MQTT is Open Source
Lots of implementations:
    Mosquitto
    Micro broker
    Really small message broker (RSMB): C
    Cloud broker services

## Slide 6: Publish Subscribe Process
A message is published once by a publisher.
Many things can receive the message.
The messaging service, or “broker”, provides decoupling between the producer and consumer(s)
A producer sends (publishes) a message (publication) on a topic (subject)
A consumer subscribes (makes a subscription) for messages on a topic (subject)
A message server / broker matches publications to subscriptions
  If no matches the message is discarded
  If one or more matches the message is delivered to each matching subscriber/consumer

## Slide 7: MQTT Topics
In MQTT, the word topic refers to the string that the broker uses to filter messages for each connected client.
Note that each topic must contain at least 1 character and that the topic string permits empty spaces. Topics are case-sensitive.
Topic Wildcards:

## Slide 8: MQTT Characteristics
MQTT protocol compresses to small number of bytes
  Smallest packet size 2 bytes
  Supports always-connected and sometimes connected
  Provides Session awareness
  “Last will and testament” enable applications to know when a client goes offline abnormally
  Typically utilises TCP-based networks.
  Max size:
    Theoretical 256MB for MQTT 5.0
    Configured at broker:
      Mosquitto: Default maximum is 1 MB
      AWS IoT: Limits MQTT messages to 128 KB

## Slide 9: MQTT Characteristics
Three quality of service levels:
  0 The message is delivered at most once, without any acknowledgment from the receiver. This means the message is sent, and no retries are attempted if it’s lost in transit.
  1 The message is delivered at least once, meaning the sender keeps resending the message until it receives an acknowledgment (PUBACK) from the receiver.
  2 The message is delivered exactly once through a four-step handshake between sender and receiver (using PUBREC, PUBREL, and PUBCOMP messages to ensure no duplication).
https://dzone.com/articles/internet-things-mqtt-quality

## Slide 10: MQTT Control Packets
The MQTT protocol uses MQTT Control Packets using the Control Header.
Control Packet consists of three parts:
  fixed header(present in all packets),
  variable header(optional)
  Payload(optional)
https://docs.devicewise.com/Content/Products/IoT_Portal_API_Reference_Guide/MQTT_Interface/MQTT-Control-Packets.htm

## Slide 11: MQTT Control Packets
MQTT Control Packet Types

## Slide 12: Connection

## Slide 13: MQTT QoS

## Slide 14: Publish-Subscribe Characteristics
A published messages may be retained
  Retained messages are used to ensure that when a client subscribes to a topic, it immediately receives the most recent message for that topic
  A publisher can mark a message as “retained”
  The broker / server remembers the last known good message of a retained topic
  The broker / server gives the last known good message to new subscribers
A Subscription can be durable
  Durable: messages forwarded to subscriber immediately, if subscriber not connected, message is stored and forwarded when connected
  Non-Durable: subscription only active when subscriber is connected to the server / broker

## Slide 16: MQTT Last Will and Testament
Notify other clients about an ungraceful disconnected client.
Client can specify its last will message when it connects to a broker.
  normal MQTT message with a topic, retained message flag, QoS, and payload
  When an “ungraceful disconnect” occurs, the broker sends the last-will message to all subscribed clients of the last-will message topic.
https://www.hivemq.com/blog/mqtt-essentials-part-9-last-will-and-testament/

## Slide 17: MQTT vs HTTP
Push delivery of messages / data / events
  MQTT – low latency push delivery of messages from client to server and server to client. Helps bring an event oriented architecture to the web
  HTTP – push from client to server but poll from server to client
Reliable delivery over fragile network
  MQTT will deliver message to QOS even across connection breaks
  Decoupling and publish subscribe – one to many delivery

## Slide 18: MQTT vs HTTP

## Slide 19: Application Example
Home care monitoring solution
  Home and patient instrumented with sensors.
    E.g. door motion, blood pressure, pacemaker/defib.
  Collected by monitoring service (broker) using MQTT
  Subscribed by a health care service in the hospital
  Alerts relations/health care profs. if anything is out-of-order

## Slide 20
Server
End Devices
Infrastructure Devices

## Slide 21: Demo