## Slide 1: Computer Networks
Frank Walsh

## Slide 2: Agenda (1st Part)
Intro
What’s a computer network
Computer Network Components
Device Types
Protocols
Topologies
Internet of Things

## Slide 3: Computer System & Networks
TCP/IP Protocol Stack
Link Layer/Ethernet
IP Networks
TCP
Application Layer Protocols
Internet of Things
Physical Computing
Sensing/Acuating
Messaging
IoT Platforms

## Slide 4: Computer Networks
Devices & Machines are effective/beautiful in isolation...
Connecting machine/ device to a computer network creates amazing possibilities...
Key points:
  Computer networks are no longer only used to connect computers
  Part of everyday life
  “Wired people should know something about wires”
This Photo by Unknown Author is licensed under CC BY-SA
1984
2021
Notes: Going back a few decades, machines worked in isolation. Cars originally were very electromechanical. Could be thought of as information islands.
Jump forward to today – everything is getting connected, not just computers, but pretty much anything you can think of. Example in modern cars – connect to roadside infrastrure and other cars. Autonamous. Also can react to events (sensors in cars can detect impact/orientation

## Slide 5: Intro

## Slide 6: QI: Arpanet
US government responds to launch of Sputnik by setting up ARPA, the Advanced Research Projects Agency
ARPANET created in 1969 connecting computers in UCLA and Stanford
In 1973, it was called the "internetwork" or "internet" for short

## Slide 7: QI: Computer Networks Growth

## Slide 8: Networks - Under the bonnet
Inherently Physical:
  Devices need some form of physical channel to communicate
  Devices need specific hardware to use that channel (eg. antenna and associated electronics)

## Slide 9: Networks – Under the bonnet
Once connected, it can get complicated!
Sophisticated combination of protocols, software, hardware, algorithms, configurations, policies...
Security, privacy, access, quality of service, wired/wireless...

## Slide 10
Server
End Devices
Infrastructure Devices

## Slide 11: Components of a Computer Network
Devices
Communicate with one another
Physical Medium
Used to connect devices
Messages
Information travelling over the medium
Rules
Governs how messages flow through a network

## Slide 12: Device Types
End Devices
Infrastructure/intermediary Devices

## Slide 13: Physical Medium
Wired
Wireless

## Slide 14: Messages
Data is divided into smaller parts during transmission
  Segmentation
The benefits of doing so:
  Many different conversations can be interleaved on the network(multiplexing)
  Increases reliability of network communications.
  The separate pieces of each message need not travel the same pathway across the network from source to destination
Adds complexity however:
  Addressing, labeling, sending, receiving.
  Reassembling
NEED RULES FOR THIS...
Application Data
Segment
Segment
Segment
Segment
Header

## Slide 15: Rules
Humans have generally accepted protocols for interaction:
  Identified sender and receiver
  Agreed upon method of communicating (face-to-face, telephone...)
  Common language and grammar
  Speed and timing of delivery
  Confirmation or acknowledgement requirements
All communication activity on the Internet is governed by protocols

## Slide 16: Human Protocol
Network Protocol

## Slide 17: Network Protocols
Machines rather than humans
All communication activity in Internet governed by protocols
Protocols define
  Format, order of msgs sent and received among network entities
  Actions taken on msg transmission, receipt

## Slide 18: Network Characteristics
Network architecture refers to:
  Design of a Network
  network's physical components and its organisation
  the technologies that support the infrastructure
  The programmed services and protocols that move the messages across that infrastructure
4 general characteristics to meet user expectations
  Fault tolerance
  Scalability
  Quality of service (QoS)
  Security

## Slide 19: Network Topology and Representations
Network diagrams, often called topology diagrams, use symbols to represent devices within the network.
Physical topology diagrams illustrate the physical location of intermediary devices and cable installation.
Logical topology diagrams illustrate devices, ports, and the addressing scheme of the network.
Notes: Physical topology diagrams illustrate the physical location of intermediary devices and cable installation.
Logical topology diagrams illustrate devices, ports, and the addressing scheme of the network.

## Slide 20: Network Topology
Will not scale well
2 devices communicate simultaneously???
What if one device goes down???
Centre is single point of failure
What connection to use? Unorganised….

## Slide 21: Typical Home Network
Source: https://techterms.com/definition/network

## Slide 22: Some Networking Vocabulary
Network Interface/Adapter: any kind of software interface to networking hardware. (e.g. wifi interface and wired interface). A network interface may be associated with a physical device, or it may be a representation of a virtual interface. (e.g. interfaces on your virtual machines)
LAN: Local Area Network refers to a network or a portion of a network that is not publicly accessible to the greater internet.
WAN: Wide Area Network. Much Larger and extensive than a LAN. Often used to refer to the Internet, as a whole.
Node: General term usually for a device on a network. Every node has a unique network address.
Media Access Control(MAC) address: Used to distinguish specific devices. A unique address that each device is assigned during manufacturing. Used to differentiates it from every other device on the internet. Typically, each network interface has a MAC address.
IP: protocols that allow the internet to work. IP addresses are unique on each network and they allow machines to address each other across networks.

## Slide 23: Key Points so far
Networks are everywhere
4 Components of every network
  Devices
  Medium
  Protocols (Rules)
  Messages (Data)
Networks are connecting everything (not just for PCs/Laptops)
Networks have a Topology
Some key characteristics of a network

## Slide 24: Internet of Things
Internet  The worldwide network of interconnected computer networks, based on a standard communication protocol (TCP/IP).
Thing  An object not precisely identifiable.
Internet of Things (IoT)  A worldwide network of interconnected objects uniquely addressable, based on standard communication protocol.

## Slide 25: What’s the difference…
Extending the current Internet and providing connection, communication, and inter-networking between devices and physical objects, or "Things,“ (even biological things!)
https://www.capitatranslationinterpreting.com/the-internet-of-things/

## Slide 26: IoT Evolution
Started with connectivity among people for sharing information.
Led to a “flat-world” where everyone across the world is connected.
Advancement in cloud computing and immersive experience led towards universal accessibility of data.
Combination of immersive experiences, connectivity and advancement in electronics further leading to Internet of Everything (IoE)
Source: Cisco

## Slide 27: IoT Potential
Conservatively  20 billion newly connected devices will be deployed.
First public website went live at CERN in 1990.
  It took 15 years to reach 1 billion people on earth over the internet.
  IoT is looking to add 6 billion connected devices per year.
Economic impact
  New revenue streams
  Reducing costs
  Reducing time to market
  Improving supply chain
  Reducing production loss
  Increasing productivity

## Slide 28: Networking and IoT
The Roles of Networks
  Managing connected devices (discovery, join, leave, etc).
  Relaying data packets from the source to the destination node in the network.
IoT is a distributed system. All nodes need to perform networking related tasks.
Main concerns as before: Reliability, Performance, Security, QOS, Scalability
http://www.psemi.com/markets/industrial/internet-of-things

## Slide 29: Learning about Networks/IoT
Can't create complex networks at home however you can simulate "virtual networks"
  Virtualbox hypervisor
  Packet Tracer
Can use programmable, multi-channel, prototyping device to investigate different mediums, protocols, IoT etc.
  Raspberry Pi has bluetooth, Wifi, Ethernet, SPI, I2C...