## Slide 1: Computer Networks
Mujahid Tabassum 2026
This Photo by Unknown Author is licensed under CC BY-NC

## Slide 2: Agenda (1st Part)
Intro
What’s a computer network
Computer Network Components
Device Types
Protocols
Topologies
Reliable Network Characteristics
Internet of Things

## Slide 3: Computer System & Networks
TCP/IP Protocol Stack
Link Layer/Ethernet
IP Networks
TCP
Application Layer Protocols
Internet of Things
Physical Computing
Sensing/Acuating
Messaging
IoT Platforms

## Slide 4: Intro
Notes: History

## Slide 5: QI: 1850s - Transatlantic Cable
The first cable was laid in the 1850s from Valentia Island to Newfoundland
Messages encoded using Morse Code using electrical signal through cable.
  it took 2 minutes to transmit just one character!(Now 30 Tb/s capacity using optical cables(optical signalling))
Encoding is the process of converting data into a specific format or code before transmission.
A Signal refers to the physical manifestation of data. E.g. electrical voltage, light pulses, or electromagnetic waves

## Slide 6: QI: 1960s - Arpanet
US government responds to launch of Sputnik by setting up ARPA, the Advanced Research Projects Agency
ARPANET created in 1969 connecting computers in UCLA and Stanford
In 1973, it was called the "internetwork" or "internet" for short
The internet is 50 years old
1st Wide Area Packet Switched Network
  data is divided into small packets for transmission

## Slide 7: Computer Networks
1984
2024
Devices & Machines are effective/beautiful in isolation...
Connecting a machine to a network creates amazing possibilities/challenges...
Key points:
  Computer networks are no longer only used to connect conventional “computers”
  Part of everyday life
  “Wired people should know something about wires”
Notes: Going back a few decades, machines worked in isolation. Cars originally were very electromechanical. Could be thought of as information islands.
Jump forward to today – everything is getting connected, not just computers, but pretty much anything you can think of. Example in modern cars – connect to roadside infrastrure and other cars. Autonamous. Also can react to events (sensors in cars can detect impact/orientation

## Slide 8: QI: Computer Networks Growth

## Slide 9: Networks - Under the bonnet
Inherently Physical:
  Devices need some form of physical channel to communicate
  Devices need specific hardware to interface to that channel (eg. Antenna, adapter, and associated electronics)

## Slide 10: Networks – Under the bonnet
Once connected, it can get complicated!
Sophisticated combination of protocols, software, hardware, algorithms, configurations, policies...
Security, privacy, access, quality of service, wired/wireless...

## Slide 11: Components of Computer Networks
Devices
Communicate with one another.
Physical Medium
Used to connect devices
Messages
Information travelling over the medium
Rules
Governs how messages flow through a network

## Slide 12: Components of Computer Networks - Device Types
End Devices
Infrastructure/intermediary Devices
Notes: An end device is where a message originates from or where it is received. Data originates with an end device, flows through the network, and arrives at an end device.
An intermediary device interconnects end devices. Examples include switches, wireless access points, routers, and firewalls.
Management of data as it flows through a network is also the role of an intermediary device, including:
  Regenerate and retransmit data signals.
  Maintain information about what pathways exist in the network.
  Notify other devices of errors and communication failures.

## Slide 13: Components of Computer Networks - Physical Medium
Wired
Wireless
Notes: Communication across a network is carried through a medium which allows a message to travel from source to destination.
Wired - Uses Electrical Impulses/Pulses of light
Wireless – Modulates specific frequencies of Electromagnetic Waves

## Slide 14: Components of Computer Networks - Messages
Data is divided into smaller parts during transmission
  Segmentation
The benefits of doing so:
  Many different conversations can be interleaved on the network(multiplexing)
  Increases reliability of network communications.
  The separate pieces of each message need not travel the same pathway across the network from source to destination
Adds complexity however:
  Addressing, labeling, sending, receiving.
  Reassembling
NEED RULES FOR THIS...
Application Data
Segment
Segment
Segment
Segment
Header

## Slide 15: Components of Computer Networks - Rules
Humans have generally accepted protocols for interaction:
  Identified sender and receiver
  Agreed upon method of communicating (face-to-face, telephone...)
  Common language and grammar
  Speed and timing of delivery
  Confirmation or acknowledgement requirements
All communication activity on the Internet is governed by protocols

## Slide 16: Human Protocol
Network Protocol
Components of Computer Networks - Rules

## Slide 17: Network Protocols
Machines rather than humans
All communication activity in Internet governed by protocols
Devices use agreed-upon protocols to communicate .
Protocols may have may have one or functions.
Protocols define
  Format, order of messages sent and received among network entities
  Actions taken on msg transmission, receipt
Function | Description
Addressing | Identifies sender and receiver
Reliability | Provides guaranteed delivery
Flow Control | Ensures data flows at an efficient rate
Sequencing | Uniquely labels each transmitted segment of data
Error Detection | Determines if data became corrupted during transmission
Application Interface | Process-to-process communications between network applications

## Slide 18: Network Topology and Representations
Network diagrams are called topology diagrams. Use accepted symbols to represent devices within the network.
Physical topology diagrams illustrate the physical location of intermediary devices and cable installation.
Logical topology diagrams illustrate devices, ports, and the addressing scheme of the network.
Notes: Physical topology diagrams illustrate the physical location of intermediary devices and cable installation.
Logical topology diagrams illustrate devices, ports, and the addressing scheme of the network.

## Slide 19: Network Topologies Examples
Physical topology diagrams
Logical topology diagrams
Notes: Physical network diagrams show all the physical assets inside buildings, floors, and rooms. Whether the devices are inside a telecom room, data center room, or office space rooms. With these diagrams, user can visualize how everything is connected — from ports of a device, cables going to and from ports, the racks/cabinets, and the equipment inside the rack, such as patch panels and servers, and all of the cabling inside the racks too.
A logical network diagram describes how information flows through a network. Logical diagrams typically show subnets (including VLAN IDs, masks, and addresses), routers, firewalls, and its routing protocols.

## Slide 20: Network Topology
Will not scale well
2 devices communicate simultaneously???
What if one device goes down???
Centre is single point of failure
What connection to use? Unorganised….

## Slide 21: Network Types
Small Home Network
  A few devices connected to each other and the Internet
Small Office/Home Office
  Connects to corporate network
  More complex intermediary devices/design(VPN/Firewalls/VLAN)
Medium to Large Network
  Many locations/networks. >100 devices
Worldwide Networks
  Millions of connected devices via interconnected networks across the globe.
  E.g. the Internet

## Slide 22: Network Types - Typical Home Network
Source: https://techterms.com/definition/network
Notes: This is example of Small home network

## Slide 23: Network Types -
LAN(local area network)
  interconnects computers within a limited area, such as a home, office building, school, or campus.
  Administered by single person or organisation
WAN(wide area network)
  covers a broad area.
  Interconnects LANs
Internet
  Global collection of interconnected LANS and WANS
  No ownership. Groups formed to maintain structure:
    IETF
    ICANN
Notes: IETF – Interne Eng Task Force Tech Standards
ICANN - Internet Corporation for Assigned Names and Numbers Namespaces/Domains

## Slide 24: Some Networking Vocabulary
Network Interface/Adapter: any kind of software interface to networking hardware. (e.g. wifi interface and wired interface). A network interface may be associated with a physical device, or it may be a representation of a virtual interface. (e.g. interfaces on your virtual machines)
LAN: Local Area Network refers to a network or a portion of a network that is not publicly accessible to the greater internet.
WAN: Wide Area Network. Much Larger and extensive than a LAN. Often used to refer to the Internet, as a whole.
Node: General term usually for a device on a network. Every node has a unique network address.
Media Access Control(MAC) address: Used to distinguish specific devices. A unique address that each device is assigned during manufacturing. Used to differentiates it from every other device on the internet. Typically, each network interface has a MAC address.
IP: protocols that allow the internet to work. IP addresses are unique on each network and they allow machines to address each other across networks.

## Slide 25: Reliable Networks - Network Characteristics
Network architecture refers to:
  Design of a Network
  network's physical components and its organisation
  the technologies that support the infrastructure
4 general characteristics to meet user expectations
  Fault tolerance
  Scalability
  Quality of service (QoS)
  Security

## Slide 26: Reliable Networks – Fault Tolerance
Refers to limiting impact failures
Implemented using Packet Switched Networks and Multiple Paths
  Packet switching splits transmitted data into packets that are routed individually over a network.
  Packets can take different routes from source to destination
Not possible with Circuit Switched Networks (eg old telecoms/phone networks)
Redundant connections provide alternative paths if a device or link fails

## Slide 27: Reliable Networks - Scalability
Networks should be able to scale(grow) easily
Performance should not be affected for existing users
Standards/protocols help to achieve this.
Adding new users/networks without degrading performance

## Slide 28: Reliable Networks - QoS
Ever watched laggy/freezing video
  Caused by higher demand for Bandwidth available
Certain traffic types require higher performance/bandwidth
Quality of Service used to do this
  QoS policy enables routers to manage flow of media traffic(voice/video)
Example: Routers prioritise voice/video traffic over web page traffic
Notes: https://community.fs.com/article/what-is-quality-of-service-qos-in-networking.html

## Slide 29: Reliable Networks - Network Security
Network infrastructure security
  Preventing unauthorized access to the physical devices
Information Security
  Security of data transmitted on network
Confidentiality – only intended recipients can read the data
Integrity – assurance that the data has not be altered with during transmission
Availability – assurance of timely and reliable access to data for authorised users

## Slide 30: Key Points so far
Networks are everywhere
4 Components of every network
  Devices
  Medium
  Protocols (Rules)
  Messages (Data)
Networks are connecting everything (not just for PCs/Laptops)
Networks have a Topology
Some key characteristics of a network

## Slide 31: Internet of Things
Internet  The worldwide network of interconnected computer networks, based on a standard communication protocol (TCP/IP).
Thing  An object not precisely identifiable.
Internet of Things (IoT)  A worldwide network of interconnected objects uniquely addressable, based on standard communication protocol.

## Slide 32: What’s the difference…
Extending the current Internet and providing connection, communication, and inter-networking between devices and physical objects, or "Things,“ (even biological things!)
https://www.capitatranslationinterpreting.com/the-internet-of-things/
Notes: Biological systems encode and send messages – maybe using chemical and molecules. Concievable we can engineer these types of networks too. In the body, encode and send data using these mechanisms

## Slide 33: IoT Evolution
Started with connectivity among people for sharing information.
Led to a “flat-world” where everyone across the world is connected.
Advancement in cloud computing and immersive experience led towards universal accessibility of data.
Combination of immersive experiences, connectivity and advancement in electronics further leading to Internet of Everything (IoE)
Source: Cisco
From an estimated 8.4 billion devices in 2017, the number of connected IoT devices is projected to reach over 25 billion by 2030

## Slide 34: IoT Potential
Conservatively  20 billion newly connected devices will be deployed.
First public website went live at CERN in 1990.
  It took 15 years to reach 1 billion people on earth over the internet.
  IoT is looking to add 6 billion connected devices per year.
Economic impact
  New revenue streams
  Reducing costs
  Reducing time to market
  Improving supply chain
  Reducing production loss
  Increasing productivity

## Slide 35: Networking and IoT
The Roles of Networks
  Managing connected devices (discovery, join, leave, etc).
  Relaying data packets from the source to the destination node in the network.
IoT is a distributed system. All nodes need to perform networking related tasks.
Main concerns as before: Reliability, Performance, Security, QOS, Scalability
http://www.psemi.com/markets/industrial/internet-of-things

## Slide 36: Learning about Networks/IoT
Can't create complex networks at home however you can simulate "virtual networks"
  Virtualbox hypervisor
  Packet Tracer
Can use programmable, multi-channel, prototyping device to investigate different mediums, protocols, IoT etc.
  Raspberry Pi has bluetooth, Wifi, Ethernet, SPI, I2C...